## Slide 1: Final Review
BHAVESH RATHORE
HEMANT SINGH
SACHIN KUMAR
VTU23631 VTU23464 VTU23753
Supervisor:
Dr. K E Purushothaman
Associate Professor
Major Project winter Semester-2025-26 Department of Electronics and Communication Engineering
Title:Edge Based Traffic Data Aggregation And Network Load Optimization For Smart Cities
Domain: Networking Date: 08-05-2026
Project Team Members
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology
1

## Slide 2: Content
Abstract
Motivation and Introduction
Objective
Literature survey
Methodology
Implementation Details and Description
Block Diagram
Software to be used
Results
References
2
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 3: Abstract
Smart cities are deploying thousands of traffic cameras at every junction to monitor vehicle flow in real time. The traditional approach of streaming raw video from every camera to a central cloud overloads the network, drives up bandwidth cost and demands heavy GPU resources. The proposed Edge-Based Traffic Data Aggregation and Network Load Optimization System solves this problem by performing vehicle detection locally at the camera using a low-cost device such as a Raspberry Pi or a normal laptop. The edge node uses YOLOv8-nano with an OpenCV background-subtraction fallback to count vehicles, classifies the junction as Low, Medium or High congestion using configurable thresholds, and transmits only the compact summary. A network optimization layer reduces traffic further using event-based transmission, a thirty-second heartbeat and gzip compression. Communication uses the lightweight MQTT publish-subscribe protocol, the central Python server stores readings in SQLite, and a Streamlit dashboard with Plotly graphs presents live status, time-series and bandwidth statistics. Experiments show over ninety percent bandwidth reduction, supporting Sustainable Development Goals 9, 11 and 13.

## Slide 4: Introduction
Cities around the world are growing rapidly and the number of vehicles on the roads is rising every year. To manage this growth, smart cities are deploying large networks of traffic cameras at every junction. The traditional approach of streaming raw video from every camera to a central cloud server overloads the network, drives up bandwidth cost and demands heavy GPU resources.
Most of this data is also redundant because the central system does not need the actual video. It only needs to know how many vehicles are present and whether the traffic is light, moderate or heavy.
The proposed Edge-Based Traffic Data Aggregation and Network Load Optimization System solves this problem by performing detection locally at the camera and transmitting only compact, compressed and event-driven summaries This makes city-scale traffic monitoring affordable, scalable and sustainable.
4
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 5: Objective
To classify traffic congestion as Low, Medium or High using simple, configurable threshold rules..
To minimize network usage through event-based transmission, a periodic heartbeat and gzip compression.
To transmit summaries over MQTT, store them in SQLite, and visualize them in real time on a Streamlit dashboard.
To demonstrate measurable bandwidth savings of over ninety percent compared to a naive system that transmits every frame.
5
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 6
6
Sl No | Authors | Title | Journal name | Year | Inference
1 | Zhang, Y. Chen | Edge Computing for Bandwidth Reduction in Smart-City Camera Networks | IEEE Internet of Things Journal | 2023 | Edge processing reduces cloud bandwidth by over 80%
2 | R.Kumar | Real-Time Vehicle Counting Using YOLOv5 on Embedded Edge Devices | International Journal of Advanced Computing | 2023 | Raspberry Pi can detect vehicles in real time using lightweight YOLO
3 | L. Chen, Y. Zhou | Comparative Analysis of MQTT and HTTP for IoT Traffic Monitoring | Journal of Network and Computer Applications | 2023 | MQTT uses 4× less bandwidth than HTTP for IoT messaging
4 | M. Khan, A. Ali | YOLOv8-Based Vehicle Detection Optimized for Edge Devices | International Journal of Computer Vision | 2024 | YOLOv8-nano runs comfortably on CPU with high accuracy

## Slide 7: METHODOLOGY
VIDEO ACQUISITION
Live video is captured at the edge using OpenCV at 2 frames per second.
VEHICLE DETECTION
YOLOv8 nano detects and counts vehicles locally on CPU, with an OpenCVMOG2 fallback.
CONGESTION CLASSIFICATION
Vehicle count is mapped to Low, Medium or High using simple thresholds.
NETWORK OPTIMIZATION
Data is transmitted only on level change or every 30 s heartbeat, and every payload is gzip-compressed.
MQTT TRANSMISSION
Compressed summaries are published over MQTT to a central broker.
STORAGE AND VISUALIZATION
Readings are stored in SQLite and displayed live on a Streamlit dashboard.

## Slide 8: Implementation Details and Description
EDGE NODE
Python edge node captures video using OpenCV and detects vehicles withYOLOv8-nano (MOG2 fallback for low-end hardware).
CLASSIFICATION
Vehicle count is mapped to Low, Medium or High congestion usingconfigurable thresholds.
NETWORK OPTIMIZATION
Data is sent only on level change or every 30 s heartbeat, with everypayload gzip-compressed.
COMMUNICATION
Compressed summaries are published over MQTT to a central broker(Mosquitto / HiveMQ).
SERVER AND STORAGE
A Python subscriber decompresses, validates and stores each readingin SQLite.
DASHBOARD
A Streamlit dashboard shows live status cards, time-series charts andbandwidth statistics.

## Slide 9: Block Diagram
8
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 10: Software to be used
Software:
10
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology
Python 3.12 – Main programming language
OpenCV 4.9 – Video capture and image processing
Ultralytics YOLOv8 – Vehicle detection (nano model)
Paho-MQTT – MQTT publish/subscribe client
Mosquitto / HiveMQ – MQTT broker
SQLite 3 – Lightweight database
Streamlit – Web dashboard framework
Plotly – Interactive charts
Pandas + NumPy – Data handling
VS Code – Development environment
Git / GitHub – Version control
Google Chrome – Dashboard viewing

## Slide 11: Output & Results

## Slide 12: Results and Discussions
12
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology
The system was tested with a single edge node and with multiple simulated edge nodes running in parallel.
Vehicle detection worked smoothly on a normal CPU-only laptop without needing any GPU.
The edge node correctly classified traffic as Low, Medium or High in real time.
The optimizer reduced network usage significantly by sending data only on level changes and gzip-compressing each payload.
The central server received, validated and stored every reading without errors.
The Streamlit dashboard displayed live vehicle counts, congestion levels and bandwidth statistics with smooth auto-refresh.
The overall system was stable, lightweight and demo-ready, proving that edge intelligence can deliver smart-city traffic monitoring at very low bandwidth.

## Slide 13: Conclusion
The Edge-Based Traffic Data Aggregation and Network Load Optimization System developed in this project demonstrates a practical and effective solution to one of the most pressing problems in modern smart-city deployments, which is the unsustainable bandwidth, storage and processing cost of streaming raw traffic video to a central cloud. By moving vehicle detection to the edge and trans-mitting only compact, compressed and event-driven summaries, the proposed system delivers the same operational insight at a fraction of the network cost.
16
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 14: References
H. Wang, L. Zhang, and Y. Chen “Edge Computing for Bandwidth Reduction in Smart-City Camera Networks”.
R. Kumar, S. Patel, and M. Verma,”Real-Time Vehicle Counting Using YOLOv5 on Embedded Edge Devices,''J. Yick, B. Mukherjee, and D. Ghosal, ”Wireless sensor network survey,” Computer Networks, vol. 52, no. 12, pp. 2292–2330,2008.
M. Khan and A. Ali,”YOLOv8-Based Vehicle Detection Optimized for Edge Devices,''R. K. Kodali and S. Mandal, ”IoT based environmental monitoring sys tem,” in Proc. 2016 Int. Conf. Control, Instrumentation, Communication and Computational Technologies, 2016.
R. Patel and S. Verma,”Lightweight SQLite-Based Storage for IoT Sensor Networks”.
K. Ainebyona, J. Mwesigwa, and P. Lubega,”Low-Cost Roadside Unit for Edge-Based Traffic Data Collection”.
17
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology

## Slide 15: Reference
P. Sharma and R. Gupta,”Threshold-Based Congestion Classification for Adaptive Traffic Control”.
A. Gubbi, R. Buyya, S. Marusic, and M. Palaniswami, “Internet of Things (IoT): A vision, architectural elements, and future directions,” Future Generation Computer Systems, vol. 29, no. 7, pp. 1645–1660, Sep. 2013.
N. Kumar, N. Chilamkurti, and J. H. Park, “ALCA: Agent learning-based clustering algorithm in wireless sensor networks,” Journal of Computer and System Sciences, vol. 79, no. 7, pp. 1040–1055, Nov. 2013.
H. Xin, F. Liu, and G. Wang,”Real-Time Vehicle Tracking Using OpenCV Background Subtraction”.
S. Vemula and M. Moraes,”Streamlit-Based Dashboards for Real-Time IoT Visualization‘’.

## Slide 16
Vel Tech Rangarajan Dr. Sagunthala R&D Institute of Science and Technology
12